Russian Technology Transfer Network - RTTN

www.rttn.ru

TECHNOLOGY OFFER

1. GENERAL DESCRIPTION

Title (max. 200 characters) Development and organizing the hi-tech full-scale SAW module production for mobile communication and telecommunication systems

Abstract of the offer Please give a brief description of the benefits of the technology including key technical or competitive advantages (max. 500 characters) Russian Federal State Enterprise offers a new type of front-end devices for UHF transceivers – a miniature integrated modules with SAW filters and RF amplifier in a SMD package. These modules are the key elements for every UHF transceiver and improve its consumer features: reduce size and weight, increase reliability and reproducibility. The enterprise is searching for investors and partners for coproduction and sale of the developed and patented modules.

Description of the offer (min. 300 characters)

Essence of the project – creating integrated modules – micromodules with SAW filters and low-noise RF amplifier in miniature SMD packages completely replacing wire items at the front-end of the UHF transceiver. The purpose is parasitic signal suppression and improving transceiver electric and technological characteristics, size and weight, and simplifying its circuitry.

Innovations and advantages of the offer (min. 50 characters)

For packaging SAW filters miniature SMD packages are widely used to combine SAW filters with surface mount technology (SMT). At the same time for miniaturizing the mobile transceivers hybrid SAW modules (functional devices combining low loss SAW filters, amplifiers, phase shifters) are successfully used. It is a promising idea to combine the two mentioned technologies in one SMD package. In this case the parasitic coupling and phase shifts are minimized, the PCB conductor ohmic losses are reduced, and what is more important, the size of the corresponding transceiver unit and its assembly costs are decreased. Alongside with the high selectivity, wide frequency range, compatibility with SMT and small size suggested SAW modules have expanded functionalities: balanced resistance input-output conversion which allows them to be successfully combined with antennas and modern balanced microcircuits of the transceiver front-end without additional matching circuits. In the experts opinion Russian and foreign analogues have no similar combination of the parameters.

Technology Keywords

Choose a maximum of five keywords applicable to the technology. This limit is mandatory

1.1.4 Other commercial communications

1.6.2 Mobile communications, pagers and cellular radio

3.1 Electronic Components

Further Information (Technical Details Concerning the Profile)

Alongside with the high selectivity up to 90 dB, wide frequency range of 120-500 MHz and fractional bandwidth of 2-7%, compatibility with SMT and small size (13.3x6.5x1.8 mm SMD package) suggested SAW modules have expanded functionalities: balanced resistance input-output conversion from 50-75 Ohm to 150-250 Ohm.

Current stage of development

Development – laboratory tested                                Available for demonstration

Available for demonstration – field tested  	  Already on the market

Additional information

Marketing analysis                       Business plan                  Available for testing or assesment

Intermediate design, research phase                                        Intermediate design, research phase

Others:

Intellectual Property Rights (only one choice)

Patents applied for but not yet granted		   Patents granted

Copyright registered					   Exclusive rights

Secret know-how					   Others:

Comments (max. 500 characters) Сountry and year of patents and applications, comments on other IPR types: Patents №№ 2093954, 2157046 Russian Federation and useful model patent № 27267 Russian Federation

2. DOMAIN OF APPLICATION

Market Application Keywords:

Choose a maximum of five keywords applicable to the technology. This limit is mandatory

1.1.4 Other commercial communications

1.6.2 Mobile communications, pagers and cellular radio

3.1 Electronic Components

Current and Potential Domains of Application (max. 500 characters) Offered SAW modules can completely replace the LC elements at the front-end of the UHF transceiver for Rescue Services, Ministry of Internal Affairs, Fire Department, riverside transport. Concerning that the Russian market of UHF transceivers makes about 50000 pcs/year the need for SAW modules will be similar.

3. COLLABORATION DETAILS

Type of collaboration sought (more than one option can be selected) 1. Licence agreement 2. Technical co-operation Joint further development Testing of new applications Adaptation to specific needs 3. Joint Venture agreement 4. Manufacturing agreement (Subcontracting & Co-contracting) Transfer of knowledge in new raw materials New way to use an existing production line Change in the partner sought's currently used technologies (installations, process, facilities) Absolutely novel process 5. Commercial agreement with technical assistance Assembly Engineering Technical consultancy Quality control Maintenance 6. Financial resources Comments: Type of partner sought: research and industrial company Specific area of activity of the partner: communication equipment manufacturer, electronic component distributor Tasks to be performed: full-scale manufacture, technological support, marketing analysis Preferred countries (for information): EEC countries, China, South Korea, USA

Additional information (picture, links)

4. ORGANISATION/COMPANY

Type Industry Technical Centre / Technology transfer centre Research institute /University Service sector Other: please specify Organisation/Company size (please tick one box) < 10 employees 10- 50 employees 50-250 employees 250-500 employees > 500 employees

5. CONTACT

| Organisation/Company Omsk Research Institute of Communications & Electronics |
| --- |
| Address 231 Maslennikov str., Omsk, 644009 | Country Russia |
| Contact first name (e.g. John) Sergei | Department SAW R&D |
| Contact name (e.g. Smith) Doberstein |  |
| Phone 7-3812-51-49-57 | Fax 7-3812-51-49-87 | E-mail info@oniip.ru URL: http:// www.oniip.ru |

I confirm that I am entitled to release the information provided on this form. I understand that it will be stored electronically and be made accessible to interested parties. Name, Position S. Doberstein, Senior Researcher Date Signature